## Slide 1: FORMULA SAE 2018

## Slide 2: ARGO Design team
Our job is to design, fabricate, test, and demonstrate.
Formula Style Car.
Non Professional “Weekend” race team.
We will be competing to sell our car to a corporation for production
Kansas State
Cal polytechnic
Perdue University

## Slide 3: Design Aspects
Performance
Aesthetics
Cost
Ergonomics
Maintainability
Manufacturability
reliability

## Slide 4: Points for Competition
Static:
  Presentation 75
  Engineering Design 150
  Cost Analysis 100
            Total: 325
Dynamic Events:
  Acceleration 100
  SkidPad 75
  Autocross 125
  Efficiency 100
  Endurance 275
            Total: 675
            ---1000

## Slide 5: Requirements
All Team Members must be registered with SAE International
sae.org/students
Valid Drivers License
Health Insurance
Faculty Advisor
Registration and fees per the SAE website
Possible waitlist(needs to be checked)

## Slide 6: Questions?

## Slide 7: (General) Specifics
Engine
Frame
Steering
Braking
Coolant
Throttle
Intake
Fuel
Exhaust
Sensors

## Slide 8: Engine
(Rule)Max Displacement is 710cc for all pistons
Selected:
2002 GSXR600 Cost and availability
600cc engine displacement
100.6Hp
Fuel Injected
CDI ignition
6-speed constant mesh transmission

## Slide 9: Frame
Steel Tube
Monocque (one_coke)

## Slide 10: Steering
(Rule) Must be mechanically connected steering
No steer by wire
Steering stops implemented to prevent a bind
Allowable 7degree play
RWS is ALLOWED
Limited to max 6degrees

## Slide 11: Braking
Four wheel braking
No Brake by wire
Brake light triangle or near round
Two independent hydraulic circuits for safety
Brake Over Travel switch
BSE Braking system Encoder
Checking brake pedal position
If implausible for greater than 100ms ETC shut down

## Slide 12: Coolant
Water only
Sealed

## Slide 13: Throttle
Carb or Throttle Body
Mechanically or Electronically
Hybrid
Return Springs
Must have two TPS with a verification shutdown
If implausibility between is greater than 10% for more than 100ms the throttle must shut off.
Two APPS, Acceleration Pedal Position Sensor (same criteria)

## Slide 14: intake
Restrictor
20mm
Intercooler is permitted
Ambient air only
No plenums

## Slide 15: Fuel
Specific fuel designed fittings and hoses are permitted
Min 91 octane
The organizer provides fuel
No additives
No temperature changes
Sight tube on filler neck
Any size tank
Vent

## Slide 16: Exhaust
No fumes for the driver at any time or any speed
No header wrap
Noise must be limited to max 110 dB
Measured by a microphone placed by the exhaust outlet

## Slide 17: Sensors
Required:
2x TPS
2x APPS
BSE
Needed:
Airflow(intake)
Exhaust(flow)
Engine Parameters
Suspension (Force, Travel, angle)
SPEED
RPM
Digital control

## Slide 18: Question?

## Slide 19: Documentation
YAY!
English majors?
Cost Report
BOM
Cost Tables
Made or bought?
Penalties for bad reporting based on cost of part
Drawings, part tooling cost, Fastener Installation,
Standard part numbering Appendix s